| 1.0 | ......................... Pcs. .............................. € .............................. € GEZE RSZ 7 smoke switch control unit, suitable for installation on fire and smoke protection closers, extendable, with telescopic function, for bridging unfavourable lintel situations, 30 mm overall height, in GEZE design, with adaption of the alarm threshold, contamination indicator and integrated test button, integrated line monitoring to ceiling-mounted detector and manual trigger switch, for connection of GEZE hold-open devices, approved by DIBt as hold-open system for fire protection closers, EN 14637 compliant Connection: 230V AC Output voltage: 24 V DC, 250 mA For lintel height > 1 m, 2 additional ceiling-mounted detectors are needed. Colour: ( ) silver-coloured ( ) white ( ) stainless steel effect ( ) RAL ….. |
| --- | --- |
| 1.1 | ......................... pcs. .............................. € .............................. € GEZE FA GC 170 wireless extension for connecting wireless components to GEZE hold-open systems without cables, consisting of: GEZE GC 171 wireless module for connection to GEZE hold-open systems, 24 VDC supply directly via GEZE hold-open system, set up with dip switch without additional programming tools, display of connection quality and status for every device, encrypted wireless connection, wireless integration of up to six devices GC 172 / GC 173 / GC 175 tested in accordance with EN 54-25 and EN 54-18, general type approval for GEZE hold-open systems ( ) GEZE GC 172 wireless ceiling-mounted smoke detector, complete with base, for wireless connection to the GEZE GC171 wireless module, encrypted wireless connection, battery-operated, battery life 5 years, tested in accordance with EN 54-7 and EN 54-25, with adaption of the alarm threshold in accordance with DIN14677, EN 14637 compliant, general type approval for GEZE hold-open systems ( ) GEZE GC 173 wireless ceiling-mounted thermal detector, complete with base, for wireless connection to the GEZE GC171 wireless module, encrypted wireless connection, battery-operated, battery life 5 years, tested in accordance with EN 54-5 and EN 54-25, EN 14637 compliant, general type approval for GEZE hold-open systems ( ) GEZE GC 175 wireless input module for wireless connection to the GEZE GC 171 wireless module, connection to manual trigger switch or potential-free contact of a fire alarm system, encrypted wireless connection, battery operated, battery life 5 years, tested in accordance with EN 54-25 and EN 54-18, installed in flush mounted socket EN 14637 compliant, general type approval for GEZE hold-open systems |
| 1.2 | ......................... Pcs. .............................. € .............................. € GEZE GC 162 ECwire smoke detector, 24 V, with 2-wire ECwire technology, complete with base, tested in accordance with EN 54-7, integrated line monitoring, DIN EN 14637 compliant, can be connected to smoke switch control unit Colour: ( ) white |
| 1.3 | ......................... Pcs. .............................. € .............................. € GEZE GC 163 ECwire thermal detector, 24 V, with 2-wire ECwire technology, complete with base, tested in accordance with EN 54-5, integrated line monitoring, DIN EN 14637 compliant, can be connected to smoke switch control unit Colour: ( ) white |
| 1.4 | ......................... Pcs. .............................. € .............................. € GEZE GC 152 smoke detector, 24 V, complete with base, tested in accordance with EN54-7, integrated line monitoring, DIN EN 14637 compliant, can be connected to smoke switch control unit (2 pcs.) Colour: ( ) white ( ) RAL ….. |
| 1.5 | ......................... Pcs. .............................. € .............................. € GEZE GC 153 thermal detector , 24 V, complete with base, tested in accordance with EN54-5, integrated line monitoring, DIN EN 14637 compliant, can be connected to smoke switch control unit (2 pcs.) Colour: ( ) white ( ) RAL ….. |
| 1.7 | ......................... Pcs. .............................. € .............................. € GEZE ORS 142 smoke switch, 24 V, complete with base, can be connected to smoke switch control unit (2 pcs) Colour: ( ) white |
| 1.8 | ......................... Pcs. .............................. € .............................. € GEZE manual trigger switch for manual triggering, ( ) SM ( ) FM |
| 1.9 | ......................... Pcs. .............................. € .............................. € GEZE hold-open magnets Operating voltage 24 V DC Power consumption 1.5 W Retention force 490 N ( ) Basic hold-open magnet model (zinc plated without base plate) for wall-mounting or installation in any structure ( ) Hold-open magnet for wall installation with base plate ( ) Hold-open magnet for flush-mounted installation ( ) Hold-open magnet for surface-mounted installation ( ) Base for hold-open magnet surface-mounting for floor mounting ( ) Hold-open magnet with zinc plated spacer tube for floor/ceiling/wall installation with swivelling magnetic head ( ) Version in basic length 185 mm ( ) Version in basic length 335 mm ( ) Hold-open magnet for wall installation basic length 65 mm GEZE magnetic counter plates ( ) Standard magnetic counter plate on mounting plate with spring system for flatness with hold-open magnet ( ) Magnetic counter plate with spring buffer on mounting plate with damping spring for soft spring-mounted end stop for heavy doors ( ) Magnetic counter plate, swivelling on mounting plate with swivelling magnetic counter plate for adjustment of angle positions between door and hold-open magnet |
| 1.10 | ......................... Pcs. .............................. € .............................. € GEZE cover caps* Colour: ( ) silver-coloured ( ) dark bronze ( ) white ( ) polished brass ( ) stainless steel ( ) RAL ..... *Cover caps can only be used for door leaf installation |
| 1.11 | ......................... Pcs. .............................. € .............................. € GEZE ECline ISM / ISM BG retrofit kit for use on the active leaf in the ISM guide rail TS 5000 or ISM guide rail BG TS 5000 for sharply dropping opening torque |